## Slide 1: Morse Code encoder
Jonathan Ceis
ENGR121 – Spring 22 – Final Project

## Slide 2: Project Objective
Integrate a computer, microprocessor, and amateur radio to facilitate the encoding and transmission of morse code.

## Slide 3: Inspiration & Concept
General Class Amateur Radio License Issued 3/4/2019
Morse code is a common method of communicating on Amateur radio bands
Amateur radio has a long history of experimentation and many major wireless advancements

## Slide 4: Morse Code Basics
  Morse code is comprised of short (dit) and long (dah) 1kHz tones
  Each character is comprised of at least 1 or more tones evenly spaced between silent periods.

## Slide 5: Architecture - Circuit
  A computer is connected to a SparkFun Redboard via USB
  The Morse code is sent from a Redboard output pin using PWM
  That signal is relayed to the amateur radio via an opto isolator.
Notes: An opto isolator is a component that allows a signal to be passed between two separate circuits without there being an electrical connection between the circuits
It essentially is a very small LED and photo resistor packaged inside of a chip.
The input powers the LED which in turn changes the resistance of the photo resistor on the other side of the chip
This is what allows the signal to be passed without an electrical connection

## Slide 6: Architecture - Circuit
  The Redboard and radio is interfaced via a custom audio cable
  A Baofeng UV-5R radio will transmits the morse code communications

## Slide 7: Architecture - Code
  Program user is prompted to enter text via the serial monitor
  Text is parsed for illegal characters and length
  Parsed text is stored within an array as individual characters

## Slide 8: Architecture - Code
  Array of text character is iterated over, encoded, and transmitted as morse code
  The program is reset and prompts the user to enter additional text.

## Slide 9: Stretch Goal – Push to Talk
Automatically Triggering PTT functionality
  In order to transmit on an amateur radio, you must push a button on the radio
  Push-to-talk functionality can be triggered by grounding Mic- to Spk-
  Code will set a pin on the Redboard to HIGH prior to transmitting and LOW when transmission is complete
  A switch or relay will connect Mic- to Spk- to activate push-to-talk functionality
Notes: Image Source: http://www.miklor.com/COM/UV_Technical.php

## Slide 10: Final Design & Demonstration
it is illegal to transmit on Amateur (“Ham”) radio frequencies without a license!
I hold a general class amateur radio license, and I am conducting this Demonstration using frequencies dedicated to experimental transmissions at low power.

## Slide 11: Problem 1 – encoding Morse
  Problem: Encoding a single text character into a properly timed series of audio tones
  Answer: Binary Representation
  Short Tone (Dit) = 1
  Long Tone (Dah) = 111
  Character Spacing = 000
  Word Spacing = 0000000
  Binary bit time = 40 milliseconds
    Approximately 30 WPM
  Solution: Create an excel file to quickly generate required variables and the function to perform the transcoding of morse code.
Character | Morse (Combined)
A | Dit Dah
Morse | 
Dit | Dah
Binary (Individual Values) | 
1000 | 111000
Binary (Combined) | 
1000111000 | 
Arduino Variable Name | 
mcA | 
Notes: Source: https://en.wikipedia.org/wiki/Morse_code#Representation,_timing,_and_speeds

## Slide 12: Problem 2 – Parsing Characters
  Problem: Text must be processed and stored in an array. The data type of the variables used must allow for this processing and parsing into an array.
  Answer: Exploratory Data Type Program
  Identify potential data types to store text and parsed data.
  Observe the results of data manipulated as that data type
  Observe the results of data converted from one data type to another
  Solution: Store all data a “String” objects. This allows for the use of “String” class functions.
Notes: Source: https://en.wikipedia.org/wiki/Morse_code#Representation,_timing,_and_speeds

## Slide 13: Problem 3 – PTT Activation
  Problem: Multiple circuit were built to facilitate push-to-talk functionality as part of the stretch goal. All circuits failed to reliably trigger or release PTT functionality.
  Attempts:
  digitalWrite & analogWrite
  Resistors, transistors, capacitors
  Opto isolator
  Radio power/ground, microcontroller power/ground
  Direct power injection
  Solution: None/Failure – It was determined that the RF interference from two radios and a computer generated an electromagnetic to field strong enough to facilitate induction within the system. The current induced caused malfunction of components.
Notes: Source: https://en.wikipedia.org/wiki/Morse_code#Representation,_timing,_and_speeds

## Slide 14: Problem 4 – Memory Limitations
  Problem: The Redboard has a very limited amount of memory. Storing many strings of data utilized too much of the dynamic memory leading to errors with the transcoding function
  Answer: Memory Optimization
  Store static text is flash memory rather than dynamic memory
  Eliminate duplicative variables
  Combine processes where possible
  Solutions:
  “F” function
  Eliminate duplicative variables
  Combine encode and transmit steps to reduce memory demand
Notes: Source: https://en.wikipedia.org/wiki/Morse_code#Representation,_timing,_and_speeds

## Slide 15: What Would I do Differently
Integration
I would not choose a project which integrated an external system
Research - Components
Additional research into components in advance would have decreased the development time required.
Research – Parsing/Memory
Researching how parsing will occur with the program in advance would have eliminated wasted time
I would not choose to integrate a system that emits radio waves (Electromagnetic Radiation)
Research and understanding of the effects of EMI on components would have eliminated wasted time
Knowledge of data types and objects would have reduced development time.

## Slide 16: Questions?

## Slide 17: Resources
  Github Repository with Code and Resources
  ARRL Amateur Radio Band Chart
  ARRL Band Plan
  CFR Part 97 – Amateur Radio Service
  Wikipedia – Morse Code
  Transistor Information
  Wikipedia - Opto Isolator
  Arduino.cc – String Objects